## Slide 1
Noel Canto Toimil
Head of Department of Innovation of HUNOSA
noelcanto@hunosa.es
Heat pumps as a way to harness mine water heat

## Slide 2
HUNOSA. Founded in 1967
Integration of coal mining private companies
Coal extraction: underground and open pit
More than 70 collieries and more than 2.000 mountain mines
Diversification activities
Geotermal energy from mine water
Biomass
Adaptation of La Pereda Power Plant for new fuels
Other renewable energies: photovoltaic, hydrogen…
BIO
MASS
ECO
COMBUSTION
GEO
THERMAL
History

## Slide 3
Geothermal energy. Our facilities
Plan for the development of district heating systems
Barredo First facilities, in Mieres (1st phase). Heating and cooling
(in operation since 2014 - 2016):
  Hospital of Mieres
  Research Building of the University of Oviedo - Campus of Mieres
  Headquarters of Asturian Energy Foundation
Barredo District Heating, in Mieres (2nd phase). Heating and domestic hot water
(in operation since 2020):
  Dwelings: Blocks of apartments
  Secondary School
  Main building of the University of Oviedo – Campus Mieres.
Langreo District Heating (1st phase). Heating and domestic hot water
(in operation since 2022)
  Residential building
  Public Health Centre
  Hotel and Geriatric Centre (elderly residence)
  Sport Centre
Geothermal facilities linked to Barredo Colliery
Geothermal facilities linked to El Fondón Colliery

## Slide 4
AWARD OF EXCELLENCE in the category of EMERGING MARKET
International Energy Agency - 6th Global District Energy Climate Awards. 2019
Participation in European Commission funded projects:
GREENJOBS (2022-2025)
POTENTIALS (2021-2023)
REWARDHEAT (2019-2023)

## Slide 5
First and second phase.
Barredo Colliery (Mieres)
First phase.
El Fondón Colliery (Langreo)
N
500 m
Geothermal energy. Our facilities
N
250 m

## Slide 6
N
500 m
Geothermal energy. First phase. Barredo Colliery
Data referred to 2021
Energy supplied:
  Heating: 5.058 MWh
  Cooling: 2.063 MWh
Reduction of CO2 emissions: 1.567 t
Investment (€)
1.452.156,94

## Slide 7
HP 1
HP 2
HP 3
Sefety water level: 35 m
4 pumps:
75 kW - 215 m3/h each
85 m – 100 m depth (1,2,4)
130 m depth (3)
15 ºC
To the river
18 ºC
1 2 4
  Headquarters of Energy Asturian Foundation
  Research Building of the University of Oviedo
  (Campus of Mieres)
23 ºC
  Hospital of Mieres
HP 1
20 ºC
To the river
18 ºC
To the river
18 ºC
23 ºC
23 ºC
HP 1
HP 2
3
Geothermal energy. First phase. Barredo Colliery

## Slide 8
Geothermal energy. Second phase: Barredo District Heating
Data referred to 2021
Energy supplied:
  Heating + domestic hot water: 1.789 MWh
Reduction of CO2 emissions: 451 t
Investment (€)
1.421.541
503.125 €
N
500 m

## Slide 9
HP 2 E
HP 1 E
Sefety water level: 37 m
2 pumps:
90 kW - 330 m3/h each
85 m – 95 m depth
23 ºC
80ºC
To the river
18 ºC
5
6
Secondary
School
Main building
Univ. Oviedo
Residential
building
M9
Residential
building
M10
Tª = 75 ºC
Tª = 80 ºC
Tª = 50 ºC
Tª = 65 ºC
Tª = 60 ºC
Tª = 40 ºC
20ºC
15ºC
17.5ºC
HP 2 C
HP 1 C
72.5ºC
65ºC
Evaporator circuit
Condenser circuit
Barredo District Heating pumping system
Barredo District Heating heat pumps
Barredo District Heating generation room
Geothermal energy. Second phase: Barredo District Heating
Barredo District Heating heat pumps

## Slide 10
Geothermal energy. Langreo District Heating. El Fondón Colliery
Estimations for 2022
Energy supplied:
  Heating + domestic hot water: 3.488 MWh
Reduction of CO2 emissions: 887 t
Investment (€)
2.235.359,82
1.136.215 €
N
250 m

## Slide 11
HP 2 E
HP 1 E
Sefety water level: 43 m
4 pumps:
30 kW - 180 m3/h each
95 m – 110 m depth
23 ºC
75ºC
To the river
18 ºC
4
1
Tª = 75 ºC
Tª = 65 ºC
20ºC
15ºC
17.5ºC
HP 2 C
HP 1 C
70ºC
65ºC
Different
facilities
2
3
Evaporator circuit
Condenser circuit
Geothermal energy. Langreo District Heating. El Fondón Colliery

## Slide 12
Thank you very much for your attention